## Slide 1: ETC Bootcode
Hari Udayakumar
20/7/2015

## Slide 2: Boot Code Data Flow

## Slide 3: On Chip uC

## Slide 4: On Chip uC
An uC 8051 subsystem is integrated
  Boot from on-chip ROM
  Code download from on-chip ROM, on-chip RAM or external ROM
  Hardware modules and external interrupt pins are mapped to uC interrupt controller

## Slide 5: Pin Strapping
At Reset the PS0 and PS1 Register are update based on the Pin Strap setting
The Pin Strap setting describes the
  Configuration of the device.
  Debug Interface Selected
  Functionality shares the LED pins, SPI and TDO signals.
Internal pull up for the pin strapping shall be disabled after reset.

## Slide 6: Pin Strapping

## Slide 7: Firmware Address Offset Configuration Register
Each GPHY Macro and uC subsystem can be configured to boot from internal ROM/RAM or external E2PROM controlled through register GPHY0_FCR/1/2/3/4
Address inversion and address offset are also configurable via the same registers.

## Slide 8: SDCC Complier
The Small Device C Compiler is specifically built for programming microcontrollers including the 8051 series microcontroller.
SDCC is a free and open source software available for download to anyone
Only limitation is the optimization.
For future use the code can be migrated to Keil C compiler

## Slide 9: Directory Structure